## Slide 1
BPv7 Implementation: Configurable Faulty Network and Evaluation
Aidan Casey
Ethan Dickey
Jihun Hwang
Sachit Kothari
Raushan Pandey
Wenbo Xie

## Slide 2: Delay/Disruption Tolerant Network (DTN)

## Slide 3
Bundle Layer

## Slide 4
Bundle Protocol (BP)
DTN Architecture
(RFC 4838)
BPv6
(RFC 5050)
BPv7
(RFC 9171)
The protocol for bundle layers
Bundles: data units of BP
IP datagram, TCP segment
Experimental Protocol
Updates from v6 to v7
Encoding method (v7 requires CBOR)
Some convergence layer adaptor (CLA) requirements
Data integrity (CRC)
Bundle format
(and so on)
November 2007
April 2007
January 2022

## Slide 5
Image source: https://youtu.be/nWtRTzXJvtI?si=tcuCufP9WPu0TtG3&t=210
Project Motivation
DTN is being studied in many places...
But what about BP(v7)?!

## Slide 6
BP(v6) is an experimental protocol.
Will it (BPv7) remain in that stage?
Is it ready for full-integration?
Image source: https://youtu.be/nWtRTzXJvtI?si=tcuCufP9WPu0TtG3&t=210
Problem Statement

## Slide 7
Contribution
Developed a BPv7 testing framework
Implemented BPv7 using Java solely based on RFC 9171
Software-Defined Networks: Easily configurable and extendable
Disruption TCP: TCP-based convergence layer for simulating disruptions
Lightweight and easy to understand
Flaws and Missing Specs in RFC 9171
Architectural flaws from software engineering point-of-views
Missing specifications and inconsistencies with RFC 4838 (DTN) and 5050 (BPv6)
Future deployment issues (implementation details)

## Slide 8: RFC 9171 Architecture Overview

## Slide 9
BPv7 Dissected
Application Agent (AA)
Bundle Protocol Agent (BPA)
Convergence Layer Adapters (CLAs)
Image source: RFC 9171

## Slide 10
Application Agent (AA)
Socket between application and bundle layers
  Receives data from BPA and makes it available to the application layer
Admin Element: 'Secretary' of BPA
  Create and process admin records
  Determines bundle error handling procedure
Image source: RFC 9171

## Slide 11
Bundle Protocol Agent (BPA)
Core of BP
Generates bundles based on data received from the AA
Makes data available to AA
  Admin element generates admin records as ADUs for BPA to send
Receives and sends bundles from and to the convergence layer (adaptors)
Image source: RFC 9171

## Slide 12
Convergence Layer Adapter (CLA)
Sends and receives bundles from transport layer on behalf of BPA
Informs BPA necessary information regarding network status (disconnected, etc.)
Can be TCP-based, UDP-based, LTP-based, etc.
Image source: RFC 9171

## Slide 13: Framework Overview

## Slide 14
Mininet [Lantz, Heller, McKeown 2010]
Software-defined networking (SDN) based network emulator
  Centralized, programmable control plane
  Control and data plane disaggregated
Arbitrary topology network of virtual devices
  Lightweight and hence scalable
  Can have them run basic software
  All these in on a single machine
    Just edit the config file (Makefile)!
Image sources: https://opennetworking.org/mininet/

## Slide 15
Open Network Operating System (ONOS) [Berde et. al 2014]
Open-source software providing the control plane for an SDN
OS for SDN controller
Allows centralized management and control
  Scalable and easily extensible
  Can run as a distributed systems across multiple servers
  Customized routing
  Just edit the config (netcfg) file!
Image sources: https://sdn.systemsapproach.org/arch.html

## Slide 16
CLA: Disruption TCP (DTCP)
 |  | E |  |  | E | E |  |  |  | E |  |  |  |  |  |  | E | 
 |  | E |  |  | E | E |  |  |  | E |  |  |  |  |  |  | E | 
 |  |  | U |  |  |  |  |  |  |  |  |  | U | U |  |  |  | 
Sender’s knowledge
Receiver's knowledge
time
Other expected disruption implementation options:
Preset disruption frequencies (config file)
Randomly determined periodic disruption frequencies
Multiple (asymmetric) types of disruptions
Asymmetrical window sizes for expected and unexpected disruptions
Our goals: Simplicity and ease of analysis

## Slide 17: Simulation

## Slide 18
Simulation: Scenario
Three hosts and one switch functioning as a gateway
Config file with routing and decision-making information
Host sends a ton of bundles
Expected delay and random delay
We varied:
  Packet density }
  Packet size
  Disruption frequency
  Simulation length

## Slide 19: Simulation results
BPA Thrashing
At 50s, the Application layer stopped sending information

## Slide 20: BPv7 (RFC 9171) Architectural Deficiencies

## Slide 21
Violation of Single-Responsibility Principle (SRP)
Suppose that our bundle layer received a bundle that is an admin record
BPA receives the bundle from CLAs
BPA then extracts the payload/ADU (admin record) from the bundle
AE receives the admin record from BPA as an ADU
AE process the received admin record
Image source: RFC 9171
Bundles
What could go wrong?

## Slide 22
Image source: RFC 9171
Violation of Single-Responsibility Principle (SRP)
Bundles
The purpose of the admin element is to deal with ACKs, status reports, and issues about bundles
However, bundles fundamentally only exist in the BPA and below
For AE to accurately deal with status reports in an intelligent way, AE needs to know:
What a bundle is, removing abstraction of the BPA, in order to deal with it
What actions make sense given a particular bundle issue
The list of sent bundles (which is in BPA)
Handling status report violates SRP!
No bundles here

## Slide 23
Image source: RFC 9171
High Coupling, Low Cohesion, and lack of an Information Expert
AE communicates with BPA by
processing admin records
AE does not communicate with
other elements in the same agent
AE primarily/solely functions as a secretary
for the BPA, i.e., belongs with the BPA
Future admin records may require
access to bundle-level metadata
Low Cohesion
AA/AE then need to deserialize information from the ADUs, or BPA needs to parse it for AA/AE
High Coupling
Lack of an Information Expert

## Slide 24
Missing Specifications
Unspecified Subject and Layer for Acknowledgement (ACK)
Suggestions
RFC 9171 (BPv7): Bundle-level metadata flag: “Acknowledgment by the user application is requested.”
RFC 4838 (DTN): Optional delay-tolerant end-to-end ACK
Send ACKs in batches in a custom format to allow for a partial set of the ACKs to be received (if it is disrupted)
ACK for delivery is optional if TCP, but highly recommended for UDP, LTP, etc.
Why is application layer responsible for ACKing? What are they ACKing?
Unclear what it means by delay-tolerant (bundled or batched, etc.)

## Slide 25
Missing Specifications
Unspecified Notion and Subject of Hop-by-hop Reliable Delivery
Questions and Concerns
Who conducts and responds to custody transfers?
BPA (based on BPv6)?
But how about admin element?
Hop-by-hop reliable transfer is required
DTN 4838: Custody transfer
Requirement removed in BPv7?
RFC 9171 does not define any notion of custody transfer
It is unclear why:
Custody transfer is left as optional or removed in RFC 9171
Relies on other layers/protocols to handle reliability
BPv7 by itself does not require DTNs to be reliable

## Slide 26: Future Works
Frameworks
More avenues of analysis
Expanded network configurations
Data corruption
Encoding
Metadata optimization
Architectural Flaws
Addressing identified architectural flaws and provide more suggestions
Is it necessary to remove custody transfer from the BP specifications?
  In what cases it could be necessary?
Try redesigning BP architecture with AE inside BPA?
  This would solve the violation of SRP for sure.

## Slide 27
Co-authors
Acknowledgements
Raushan Pandey
Wenbo Xie
Sachit Kothari
Aidan Casey
Special Thanks
Alan Hylton
@ NASA GSFC
For productive convos
and helpful advice
Anonymous reviewers
For constructive feedback

## Slide 28: Appendix

## Slide 29
Too 'heavy' and intricate to use just for studying BP
Treats BP as a blackbox --- unclear where the 'disruption' tolerance comes from
Why did we need to create a new implementation?
DTNs are being studied widely, and implementations of DTNs include BP.
Why did we implement BPv7 from scratch?
Outdated
Implemented based on expired IETF drafts
Less popular languages (and less beginner-friendly)
Kotlin, C, etc.
Incorrect
E.g., BPA and AA communicating by sending bundles, not ADUs/admin records

## Slide 30: Configurable Options
High-impact network options:
DTCP options
  Down probabilities of E, U disruptions
  Window size
Configurable options (Simulation Main controls):
  Bundle lifetime
  Sending delay range between bundles

## Slide 31
Simulation Results
0 – low density of packets (every )
1 – large packets ()
1 – high frequency of disruptions ()
1 – high density of packets (every )
1 – large packets ()
1 – high frequency of disruptions ()
At 50s, the Application layer stopped sending information

## Slide 32
More Simulation Results

## Slide 33
Missing Specifications
Unspecified Conv. Layer (CL)
Suggestions (request for answers)
CL/CLAs are left as implementation details
But DTN is an overlay architecture
CL provides congestion control in BPv7
Responsibility of the transport layer
How should the CL(A) receive packets? Should it hold onto partial packets?
What are the responsibilities of CLA (that are not for BPA and AA)? (E.g., routing.)
Should the CLA be responsible for knowing anything about and/or handling (un)expected network disruptions?

## Slide 34
Missing Critical Features
Undefined method of clock accuracy
Scheduled contacts may require time-synchronization throughout the DTN
Bundles have timestamps and lifetime; need to be accurate for many purposes
Clock synchronization is not an easy/trivial problem
  New notion of clock accuracy might be needed
Absence of identification of routing responsibilities
Only high-level mathematical intuition on routing in DTN was provided.
Unclear which layer/agent in BP is responsible for routing